## Slide 1: Air Quality Modeling Studies in South Korea
2013. 2. 4
Soontae Kim
Dept. of Environmental Engineering
Ajou University, Suwon, South Korea
Workshop at National Central University, Taiwan

## Slide 2
Ozone season in Houston
February ~ November
Air Quality Forecasting System
Long-range Transport of Air Pollutants
PM, NO2, and Ozone SIP over Seoul Metropolitan Area

## Slide 3
WRF & MCIP
GFS
downloading
MEGAN
SMOKE
CMAQ
Merge
IDL
Web
Emissions
Flexi-nesting
AERO6
(Heavy Metals)
CAMx
DDM
Exposure
w/ Population
BFM
- UM
- FNL
UCM
Physical options
SST
Fire Emission
BEIS3
Air Quality Forecasting in Ajou University
Sulfate Tracking
PCA

## Slide 4: Horizontal Grid Structure
First True Latitude (Alpha): | 30°N
Second True Latitude (Beta): | 60°N
Central Longitude (Gamma): | 126°W
Projection Origin: | (126°W, 38°N)
Spheroid: | Perfect Sphere, Radius = 6,370,997 meters
CMAQ Domain Name | Range (km) |  | Number of Cells |  | Cell Size (km) | 
 | Easting | Northing | Easting | Northing | Easting | Northing
KNU_27_01 | (-2349000, -2344302) | (-1728000, -1724544) | 174 | 128 | 27 | 27
KNU_09_01 | (-180000, -179397) | (-585000, -584262) | 67 | 82 | 9 | 9
NIER_03_01 | (0, 174) | (-135000, -134817) | 58 | 61 | 3 | 3
Notes: 모델의 Map projection은 lambert conformal conic projection을 사용하였으며, 수평해상도는 27-km, 9-km, 3-km으로 설정하여 Nesting-down 하였다(그림 @). lambert conformal conic projection은 북위 30~ 60도, 경도 126도 projection의 중앙은 126도 38도 지구는 완벽히 둥글다고 가정하고 반지름은 6370997m이다
표 1은 각 수평도메인에 대한 설명을 정리한 것이다. 27-km domain의 셀 개수는 동-서로 174개 북-남으로 128개이며, 9-km의 경우 셀 개수는 동-서로 67, 북-남으로 82개 이며, 3-km는 동-서로 58개, 북-남으로 61개의 셀을 가진다.

## Slide 5
 | Options | Test options
WRF | Version 3.4.1 | 
Landuse | KMOE / SRTM | 
Micro physics | WSM3 (Hong et al. 1998; Hong et al. 2004) | WSM6
Cumulus scheme | Kain-Fritsch (Kain 2004) | 
Long wave radiation | RRTM (Mlawer et al. 1997) | 
Short wave radiation | Dudhia Scheme | Goddard
PBL scheme | YSU (Hong et al. 2006) | 
LSM scheme | NOAH (Chen and Duhia 2001) | 
WRF Configurations
Notes: 표는 기본적인 AQF 구축에 이용된 WRF 모델의 물리 옵션을 보인 것이다.
기본적인 물리 옵션 외에도 다른 옵션들에 대한 테스트를 수행하며,
초기장과 입력자료에 따른 결과도 비교할 예정이다.

## Slide 6
Input data
Area
Nonroad
Mobile
Point
Annual
Emissions
Shape files
AQM
MIMS Spatial
Allocator
Annual, Monthly
Annual
Annual
Spatial allocation
; domain-specific
Temporal allocation
; hourly resolved emissions
Chemical speciation
; CB4, SAPRC99, RADM2
Plume rise
; w/ meteorology
SMOKE processing
Input preparation
Format conversion
DB/ASCII  IDA
SCC mapping
Split factors for
chemical speciation
Temporal profiles
Surrogates
Spatial allocation for
county-based emissions
SMOKE w/ Korean NEI
Sparse Matrix Operator Kernel for Emissions
Korean Emissions Inventory Processing using the US EPA's SMOKE System (2008), Asian Journal of Atmospheric Environment, 2(1), 34-46.

## Slide 7
First day
Second day
WRF / MCIP (60hr)
1
2
3
CMAQ / SMOKE / MEGAN (57hr)
AQF w/ GFS
Data download: 15 KST (updated between 14 KST ~ 15 KST)
48-hr Forecasting:
Ex) Jun 8th 00 KST ~ Jun 10th 00 KST → Jun 7th 15 UTC ~ Jun 9th 15 UTC)
00 UTC
00 KST
00 UTC
00 KST
09 KST
09 KST
00 UTC
00 KST
09 KST
12 UTC
12 UTC
12 UTC
Diagnostic Models (24hr)
Daily AQF Schedule
Notes: WRF와 MCIP자료를 60시간 데이터를 도출하고 그 결과자료를 이용하여 CMAQ, SMOKE, MEGAN의 57시간 결과를 얻어낸다.
초기장(GFS)를 00시 부터 81시 까지 데이터를 다운받고, 그 중 12UTC부터 72UTC까지 60h를 WRF와 MCIP을 통해 데이터를 얻는다.
MCIP 처리과정에서 생성된 기상자료 중 최초 3시간은 생략되고 나머지 57h를 CMAQ, SMOKE, MEGAN을 이용해 data를 얻어내
다음날 00KST부터 48KST까지 2일간의 예보자료를 얻어 낸다.

## Slide 8
System Update & Evaluation
 | Base | AQFv6
WRF | Version 3.3 | Version 3.4.1
Microphysics | WSM3 | WSM6
Emissions | CAPSS 2007 | CAPSS 2008
3-km Land use |  | Revised
MCIP | LPBL 1 & 2 | LPBL 1
SMOKE |  | w/ new MCIP
MEGAN |  | w/ new MCIP

## Slide 9
Base AQFv6

## Slide 10
5/2~11/29
Systematic Bias Correction for AQI

## Slide 11
PM10 Forecast Accuracy for Sub-regions

## Slide 12
ASO4
China SOx
S. Korea SOx
Japan SOx
Sulfate & Sensitivity to SOx emissions - DDM
1st-order sensitivity (surface layer)
Notes: 그림 1) 다음 그림은 한국, 중국, 일본을 포함하는 동아시아 지역의 ASO4농도를 수평적으로 나타낸 그림이다. 중국 중남부 지역에서 SO4농도가 30ug/m3로 가장 높은 농도를 보이며, 남한 중북부 지역에서 3ug/m3 이하의 농도가 나타나 삼국 중 가장 낮은 농도를 보이는 것으로 나타났다.
그림 2) 위의 결과를 바탕으로 다음 그림과 같이 중국, 남한, 일본으로 영역을 구분하여 Surface layer의 각 국의 Sox 배출량이 수도권 Sulfate 농도 변화에 대한 1차 민감도 분석을 수행하였다.
그림 3) 그림 3은 수도권 지역을 대상으로 ASO4의 모사 농도와 함께 3국의 Sox 배출량에 따른 수도권 ASO4 농도 변화에 대한 민감도 계수를 함께 나타낸 것이다.
수평적으로 나타낸 그림으로부터 중국 Sox 배출량이 수도권의 ASO4 농도 변화에 대한 민감도가 가장 큰 것을 알 수 있다. 모사 대상 일의 ASO4농도는 1~3ug/m3 정도로 모사되었으며, 중국 배출량의 민감도가 지배적인 것으로 나타났다.
해당 모사일 17시의 ASO4 모사 농도는 약 3ug/m3이며, 중국 배출량에 대한 민감도가 2ug/m3으로 분석되었다. 이는 중국의 Sox배출량을 10% 감소시킬 경우, 수도권 지역에서 ASO4의 농도가 0.2ug/m3 감소할 수 있다는 것을 의미한다.

## Slide 13
Sulfate/Nitrate & Sensitivities - DDM

## Slide 14
Ozone & ZOC - DDM

## Slide 15
ASO4
ASO4 EMI
ASO4 GAS
ASO4 ICBC
ASO4 OX
Sulfate Tracking
Notes: 다음은 국내 ASO4의 농도 분포를 수평적으로 나타내고, ASO4의 배출량, ASO4 gas, ASO4의 배경농도와 ASO4 산화물로 구분하여 수도권 지역의 ASO4 농도에 대한 이들의 영향을 분석한 내용이다. 먼저 국내의 ASO4 농도 분포를 나타낸 그림에서 서울 및 수도권 지역의 ASO4농도가 20ug/m3이상인 것으로 나타나 비교적 고농도로 분포하고 있는 것으로 분석되었고, ASO4 산화물의 영향이 가장 높은 것으로 나타났다. 해당 모사일에 수도권 지역의 ASO4 모사 농도는 최저 1ug/m3 이상에서 최고 4.5ug/m3 이상으로 모사되었으며, 오전 00시에 가장 높은 모사 농도를 보이고 오전 06시까지 급격한 감소 추세를 보인다. 이때, 모사된 농도에 가장 높은 영향은 ASO4 산화물에 의한 것으로 분석되었으며, 오전 06시 이후 ASO4의 배경농도의 기여도가 점차 증가하고, 12시 이후 ASO4 gas와 ASO4 배출량의 기여도가 나타난다. 여기서 주목할 점은 오전 시간대에서 야간으로 갈수록 지배적이었던 ASO4 산화물의 영향이 줄고 배경농도의 기여도가 점차 증가하여 야간 시간대에는 지배적인 영향을 미친다는 점이다.

## Slide 16
Primary Carbon Apportionment

## Slide 17
NOX Iso-surface over SMA
Iso-surface: 30 ppb
June 4, 2004 at 02 KST
Seoul
Major point sources

## Slide 18
Vertical mixing up to ~2.5 km
Strong O3 titration
High O3
June 4, 2004 at 13 KST
Horizontal & Vertical Ozone over SMA
NO + O3  NO2 + O3
http://venus.ajou.ac.kr/aqf/AQFv1/

## Slide 19: Contribution and Sensitivity
Environ (2010)
The homogeneous rate terms kxA2 and kxB2 clearly describe chemical change for pollutants from sources A and B (xA and xB),
But the inhomogeneous rate term 2kxAxB is not uniquely associated with either source A or B.
Consider a chemical species X that has two sources A and B (so X = xA + xB) and which undergoes a second order self-reaction with rate constant k.

## Slide 20
Emissions, Meteorology, IC/BC, etc.
CMAQ
∆
Check scientific understanding
Extend beyond observations
Forecasting and prediction
∆ (e.g., Seoul Emissions)
CMAQ-HDDM
Atmospheric response
Control strategies
Source apportionment
Concentrations
Sensitivities
Cohan et al. (2005)

## Slide 21: Sensitivity Analysis
Sensitivity coefficients ( = )
Control strategy ( )
Source apportionment (++)

## Slide 22: Sensitivity Coefficients
Ebase
Cbase
Concentration
Emission
S(1)=
S(1) > 0
S(1) < 0
S(1) = 0
explains local sensitivity

## Slide 23: Sensitivity Coefficients
BFM (Brute Force Method)
HDDM (High-order Decoupled Direct Method)

## Slide 24: Sensitivity Coefficients
E(base)
E(+10%)
E(-10%)
C(+10%)
C(base)
C(-10%)
Concentration
SHDDM(1)=
SBF(1)=
△εE(base)
-△εE(base)
△E
△C
Emission

## Slide 25: Ozone 1st-Order Sensitivity Coefficients
BFM
HDDM
NOx
VOC
Kim (2011)

## Slide 26: Sensitivity Coefficients
E(base)
E(+10%)
E(-10%)
C(+10%)
C(base)
C(-10%)
Concentration
SHDDM(1)=
SBF(1)=
△εE(base)
-△εE(base)
△E
△C
Emission
SHDDM(2)=
=

## Slide 27: Ozone 2nd-Order Sensitivity Coefficients
BFM
HDDM
NOx
Kim (2011)

## Slide 28: Ozone 2nd-Order Sensitivity Coefficients
BFM
HDDM
VOC
Kim (2011)

## Slide 29: Sensitivity Coefficients: BFM vs HDDM
Kim (2011)
 |  | Ozone sensitivity1 (ppb) to |  |  | 
 |  | NOx emissions |  | VOC emissions | 
 |  | 1st Order | 2nd Order | 1st Order | 2nd Order
Mean sensitivity | BFM | 6.70 | 4.32 | 3.41 | 0.99
 | HDDM | 6.85 | 4.44 | 3.45 | 0.99
Maximum sensitivity | BFM | 3.86 | 39.86 | 9.04 | 1.9
 | HDDM | 3.86 | 42.65 | 9.12 | 2.04
NMB (%) |  | -2.42 | 4.94 | 1.03 | 0.2
NME (%) |  | 2.76 | 9.16 | 1.67 | 8.98
R2 |  | 0.9998 | 0.995 | 0.9992 | 0.9956

## Slide 30: Control Strategy
Ebase
Cbase
Concentration
Emission
explains change in concentration after a emissions reduction plan
△E
△C
EP
CP
BFM: C(base), C(p), …
HDDM:
)

## Slide 31: Control Strategy
In case more than two emissions are to be reduced, cross sensitivity is required
Kim et al. (2011)

## Slide 32: Source Apportionment
Ebase
Cbase
Concentration
Emission
Zero-out Contribution of a target emission
△E
(= a target emission)
△C = ZOC
EP
CP
Need to check if VOC-limited or NOx-limited
A large perturbation may go across the regime
Kim et al. (2011)

## Slide 33: Ozone Simulations over the SMA
Kim et al. (2011)

## Slide 34: NOx and VOC reductions: BFM vs HDDM
NOx
VOC
Kim et al. (2011)

## Slide 35: NOx and VOC reductions: BFM vs HDDM
Truck emissions
~ 25% NOx emissions from the SMA
Kim et al. (2011)

## Slide 36
Base Run – Ozone Concentrations

## Slide 37
Anthropogenic emissions: Emissions from Seoul, Gyeonggi, and Incheon (SMA) only
Biogenic emissions: Domain-wide
NO Conc.
Area source
Mobile source
NO2 Conc.
Point source
Biogenic emissions
Contributions to NOx Concentrations
June 3rd, 2000 at 21 KST
Contributions to NOx Concentrations

## Slide 38
Chart: Relatvie Contributions (%)
| Area | Mobile | Point | Biogenic | BC
SMA | 33.7 | 53.7 | 9.1 | 0 | 3.6
Seoul | 34.7704 | 62.9803 | 1.687 | 0 | 0.56232
June 3rd~10th, 2004
Averaged over Seoul Metropolitan Area (SMA) & Seoul
Contributions to Daily Max NOx Concentrations

## Slide 39
Mobile (+area) sources  the major reduction factor for ozone over Seoul
Area
Mobile
Biogenic
Boundary
Point
June 4th, 2004 at 15 KST
O3 Conc.
Anthropogenic emissions: Emissions from Seoul, Gyeonggi, and Incheon (SMA) only
Biogenic emissions: Domain-wide
Contributions to O3 Concentrations
Contributions to O3 Concentrations

## Slide 40
Averaged over Seoul Metropolitan Area & Seoul
Note: Boundary conditions (> 50%) and cross-terms are not shown.
June 3rd~4th, 2004
Chart: Relative Contributios (%)
| Area | Mobile | Point | Biogenic
SMA | 11.8591 | 8.7905 | 18.6335 | 16.1302
Seoul | 2.3992 | 1.3734 | 8.7117 | 20.991
Contributions to Daily Max O3 Concentrations

## Slide 41
The cross-term (Seoul + Gyeonggi) becomes important to explain O3 over Southern Gyeonggi
June 4th, 2004 at 15 KST
Seoul Emissions
Gyeonggi Emissions
Incheon Emissions
Contributions to O3 Concentrations
Seoul + Gyeonggi
O3 Conc.
Biogenic emissions are excluded
Contributions to O3 Concentrations

## Slide 42
Biogenic emissions are excluded
June 3rd~4th, 2004
Chart: Relavtive Contributios (%)
| Seoul | Gyeonggi | Incheon | G x S | G x I | S x I
SMA | 3.0857 | 17.5272 | 13.8982 | 24.641 | 2.949 | 1.3857
Seoul | -0.32004 | 18.5799 | 7.6164 | 23.3665 | 0.78642 | 0.4541
Contributions to Daily Max O3 Concentrations
NO + O3  NO2 + O3
NO2  NO + O
O + O2  O3

## Slide 43
After anthropogenic VOC emission reductions for Seoul Metropolitan Area
June 3rd, 2004
Chart: Relative changes in VOC emissions (%)
| -10 | -30 | -50 | -70 | -90
SMA | -3.8 | -10.4 | -15.5 | -18.6 | -20.8
Seoul | -5.6 | -15.9 | -24.8 | -31.2 | -36.3
Chart: Relative changes in VOC emissions (%)
| -10 | -30 | -50 | -70 | -90
SMA | -3.4 | -9.4 | -13.2 | -15.2 | -16.7
Seoul | -4.6 | -12.4 | -18.9 | -24.1 | -28.7
June 4th, 2004
Changes in Daily Max O3 Concentrations

## Slide 47
Itahashi et al. (2012)

## Slide 49: Thank You!