## Slide 1: From MODIS to VIIRS – New Satellite Aerosol Products
Ho-Chun Huang and
NOAA STAR Aerosol Cal/Val Team
March 18, 2014
National Central University, Chungli, Taiwan

## Slide 2: Outline
NOAA/NASA Joint Polar Satellite System (JPSS)
Visible Infrared Imaging Radiometer Suite (VIIRS) instrument
  History, aerosol algorithms and products
Difference between VIIRS and MODIS
VIIRS Performance Evaluation on Aerosol Optical Thickness
Summary
Description of obtaining VIIRS data

## Slide 3: VIIRS Aerosol Cal/Val Team
Name | Organization | Major Task
Kurt F. Brueske | IIS/Raytheon | Code testing support within IDPS
Ashley N. Griffin | PRAXIS, INC/NASA | JAM
Brent Holben | NASA/GSFC | AERONET observations for validation work
Robert Holz | UW/CIMSS | Product validation and science team support
Nai-Yung C. Hsu | NASA/GSFC | Deep-blue algorithm development
Ho-Chun Huang | UMD/CICS | SM algorithm development and validation
Jingfeng Huang | UMD/CICS | AOT Algorithm development and product validation
Edward J. Hyer | NRL | Product validation, assimilation activities
John M. Jackson | NGAS | VIIRS cal/val activities, liaison to SDR team
Shobha Kondragunta | NOAA/NESDIS | Co-lead
Istvan Laszlo | NOAA/NESDIS | Co-lead
Hongqing Liu | IMSG/NOAA | Visualization, algorithm development, validation
Min M. Oo | UW/CIMSS | Cal/Val with collocated MODIS data
Lorraine A. Remer | UMBC | Algorithm development, ATBD, liason to VCM team
Andrew M. Sayer | NASA/GESTAR | Deep-blue algorithm development
Hai Zhang | IMSG/NOAA | Algorithm coding, validation within IDEA

## Slide 4: NOAA/NASA Joint Polar Satellite System (JPSS)
NOAA/NASA JPSS Program
JPSS/NPP will provide a continuation of major long-term observations by
the NASA Earth Observing System (EOS)

## Slide 5
NOAA/NASA JPSS Program
Oct 2011
2017
2021

## Slide 6
JPSS Instrument |  | Measurement
 | ATMS - Advanced Technology Microwave Sounder | ATMS and CrIS together provide high vertical resolution temperature and water vapor information needed to maintain and improve forecast skill out to 5 to 7 days in advance for extreme weather events, including hurricanes and severe weather outbreaks
 | CrIS - Cross-track Infrared Sounder | 
 | VIIRS – Visible Infrared Imaging Radiometer Suite | VIIRS provides many critical imagery products including snow/ice cover, clouds, fog, aerosols, fire, smoke plumes, vegetation health, phytoplankton abundance/chlorophyll
 | OMPS - Ozone Mapping and Profiler Suite | Ozone spectrometers for monitoring ozone hole and recovery of stratospheric ozone and for UV index forecasts
 | CERES - Clouds and the Earth’s Radiant Energy System | Scanning radiometer which supports studies of Earth Radiation Budget
Courtesy of Mitch Goldberg

## Slide 7
Satellite Aerosol Retrieval
TOA Reflectance
Surface Reflectance
Aerosol Optical Thickness

## Slide 8: Visible Infrared Imaging Radiometer Suite (VIIRS)
cross-track scanning radiometer with ~3000 km swath – full daily sampling
7 years lifetime
22 channels (412-12,016 nm)
  16 of these are M bands with 0.742 x 0.776 km nadir resolution
  aerosol retrieval is from M bands
high signal-to-noise ratio (SNR):
  M1-M7: ~200-400
  M8-M11: ~10-300
2% absolute radiometric accuracy
single look
no polarization
Band name | Wavelength (nm) | Bandwidth (nm) | Use in algorithm
M1* | 412 | 20 | L
M2* | 445 | 14 | L
M3* | 488 | 19 | L, TL TO
M4* | 555 | 21 | TO
M5* | 672 | 20 | L, O, TO
M6 | 746 | 15 | O
M7* | 865 | 39 | O, TL
M8 | 1,240 | 27 | O, TL, TO
M9 | 1,378 | 15 | TL
M10 | 1,610 | 59 | O, TL, TO
M11 | 2,250 | 47 | L, O, TL, TO
M12 | 3,700 | 191 | TL
M13 | 4,050 | 163 | none
M14 | 8,550 | 323 | none
M15 | 10,763 | 989 | TL, TO
M16 | 12,016 | 864 | TT, TO
*dual gain, L: land, O: ocean; T: internal test
Istvan Laszlo

## Slide 9: VIIRS Granule
Example VIIRS granule, 11/02/2013, 19:05 UTC
RGB image
Sensor Data Records (SDRs), converted from raw VIIRS data (RDR), are used in the VIIRS aerosol algorithm.
Processing is on a granule by granule basis. VIIRS granule typically consists of 768 x 3200 (along-track by cross-track) 0.75-km pixels
Istvan Laszlo

## Slide 10: VIIRS Environmental Data
Land
Active Fire
Land Surface Albedo
Land Surface Temperature
Vegetation Index & Fraction
Surface Type
Ice Surface Temperature
Sea Ice Characterization
Snow Cover/Depth
Ocean
Sea Surface Temperature
Ocean Color/Chlorophyll
Clouds
Cloud Mask
Cloud Optical Thickness
Cloud Effective Particle Size Parameter
Cloud Top Height
Cloud Fraction
Polar winds
Aerosols
Aerosol Optical Thickness (AOT)
Aerosol Particle Size Parameter (APSP)
Suspended Matter (SM)

## Slide 11
At NOAA Comprehensive Large Array-data Stewardship System (CLASS):
Intermediate Product (IP)
  0.75 km pixel (768x3200)
    AOT, APSP, AMI (Aerosol Model Information), and quality flags
Environmental Data Record (EDR)
  6 km aggregated from 8x8 IPs filtered by quality flags (96x400)
    AOT, APSP, and quality flags
  0.75 km pixel (768x3200)
    SM
At NOAA/NESDIS/STAR
Gridded 550-nm AOT EDR
  regular equal angle grid: 0.25°x0.25° (~28x28 km)
  only high quality AOT EDR is used
Istvan Laszlo
VIIRS Aerosol Products

## Slide 12: VIIRS Aerosol Algorithm
Separate algorithms used over land and ocean
Algorithm heritages
  over land: MODIS atmospheric correction
  over ocean: MODIS aerosol retrieval
The VIIRS aerosol algorithm is similar but NOT identical to the above MODIS algorithms
Many years of development work:
  Initial science version is by Raytheon
  Updates and modifications by NGAS
  Current Cal/Val Team is to maintain, evaluate and improve the algorithm
See Jackson et. al. (2013) for detail
Istvan Laszlo

## Slide 13
VIIRS versus MODIS
 | VIIRS | MODIS
Algorithm (general) |  | 
Main source of data screening | External VCM | Internal tests
Aggregation on | Outputs | Inputs
Residual calculated as | Absolute difference | Relative difference
Over-ocean algorithm |  | 
Channel used | 0.67, 0.74, 0.86, 1.24, 1.61, 2.25 µm | 0.55, 0.66, 0.86, 1.24, 1.61, 2.12 µm
Surface reflection | Non-lambertian, function of wind speed and direction | Lambertian, independent on wind (will change in C6)
Aerosol model | Combination of fine and coarse modes | Combination of fine and coarse modes
Match to | TOA reflectances | TOA reflectances
Retrieval over inland water | No | Yes
Over-land algorithm |  | 
Channel used | 0.41, 0.44, 0.48, 0.67, 2.25 µm | 0.47, 0.66, 2.12 µm
Aerosol model | Select one from five pre-defined models | Mix two assigned fine and coarse mode dominated models
Spectral surface reflectance | Constant ratios of 0.41, 0.44, 0.48, 2.25 µm over 0.67 µm (will depend on NDVI) | Linear relationship between 0.66 and 2.12 µm as a function of NDVI and scattering angle; constant linear relationship between 0.47 and 0.66 µm
Match to | Surface reflectances | TOA reflectances
Istvan Laszlo

## Slide 14: VIIRS versus MODIS
 | VIIRS | MODIS
Products |  | 
Nominal spatial resolution | 0.75 km (IP) 6 km (EDR) | 10 km (C5) 3 km (C6)
Granule size | 86 seconds | 5 minutes
AOT range | [0, 2] (will change) | [-0.05, 5]
Main product land | Spectral AOT | Spectral AOT
Main product ocean | Spectral AOT Ångström exponent | Spectral AOT Fine mode fraction
Orbit |  | 
Orbit altitude | 824 km | 690 km
Equator crossing time | 13:30 UTC | 13:30 UTC (Aqua)
Swath width | 3000 km | 2300 km
Pixel resolution (Nadir) | 0.75 km | 0.5 km
Pixel resolution (swath edge) | 1.5 km | 2 km
EDR AOT product (nadir) | 6 km | 10 km
EDR AOT product (swath edge) | 12 km | 40 km
Istvan Laszlo

## Slide 15
Don Hillger, Tom Kopp, and the EDR Imagery Team

## Slide 16: VIIRS versus MODIS
Suomi-NPP (13:30 Local Time, Ascending)
Aqua (13:30 Local Time, Ascending)
VIIRS
MODIS

## Slide 17: AOT & APSP Products Timeline
Initial instrument check out; Tuning cloud mask parameters | Beta status | Error | Beta status | Provisional status
17
28 Oct 2011
2 May 2012
15 Oct 2012
28 Nov 2012
23 Jan 2013
Red periods: | Product is not available to public, or product should not be used.
Blue periods: | Product is available to public, but it should be used with caution, known problems, frequent changes.
Green period: | Product is available to public; users are encouraged to evaluate.
*No reprocessing at this moment

## Slide 18: What is the difference between VIIRS and MODIS?

## Slide 19: The AOT retrieval between VIIRS and MODIS
VIIRS AOT EDR at 550nm (550) (~6 km resolution)
The Level 2 Aqua MODIS Dark Target 550 (~10 km resolution)
In-situ AOT () Measurement as Reference Data
  Near-real time Level 1.5 AERONET (The Aerosol Robotic Network) direct-sun measurements
  Level 2 MAN (The Maritime Aerosol Network) series average data
Evaluation Periods
  Over ocean, from 05/02/2012 to 09/01/2013
  Over land, from 01/23/2013 to 09/01/2013 (after a critical update)
  Exclude the data processing error period
See Liu et. al. (2014) for detail

## Slide 20: VIIRS versus MODIS
Time series of the daily mean 550 retrieval bias (solid lines) and standard deviation (whiskers) of all VIIRS-AERONET and MODIS-AERONET match-up over ocean (a) and land (b).
Comparable performance of the two satellite retrievals over ocean (excluding the VIIRS processing error period) and land (after the PCT update on 01/22/2013)
Liu et al, 2014

## Slide 21
550 Comparisons for Collocated
VIIRS-AERONET and MODIS-AERONET Data
Chart: 
| Sample Size
VIIRS Ocean | 1652
MODIS Ocean | 1281
VIIRS Land | 4647
MODIS Land | 3624
Chart: 
| Accuracy | Precision | Uncertainty
VIIRS Ocean | 0.007 | 0.047 | 0.048
MODIS Ocean | -0.001 | 0.053 | 0.053
VIIRS Land | -0.028 | 0.098 | 0.102
MODIS Land | -0.014 | 0.099 | 0.1
Chart: 
| Correlation | Percentage Within Range
VIIRS Ocean | 91.9 | 72.8
MODIS Ocean | 90.7 | 66.6
VIIRS Land | 86.6 | 77.2
MODIS Land | 89.2 | 67.2
Over ocean, the accuracy of VIIRS and MODIS are both less than 0.01. Over land, the accuracy of VIIRS is ~ -0.03 and for MODIS is ~ -0.01.
For the reset of statistics, the scores of VIIRS are similar to those of MODIS.

## Slide 22
550 retrieval error over individual AERONET sites
Slightly overestimation over costal area
Positive bias in Northern America
Negative bias in Eastern US
Higher positive bias in Southeast Asia
Higher negative bias in Northern India
Liu et al, 2014

## Slide 23: The AOT retrieval performance of VIIRS versus AERONET and MAN

## Slide 24
Scatter plots of 550 of individual VIIRS-AERONET match-ups over ocean (a) and land (b). Each scatter covers a width of 0.01 AOT, and the number of match-ups falling within is represented in color. The 1:1 line and linear regression are displayed.
Positive and negative bias of ~ 0.01 is found for over ocean and land, respectively. Precision and uncertainty are ~ 0.061 (0.130) for over ocean (land). Correlation is ~0.906 (0.773) for over ocean (land).
Liu et al, 2014
(Coastal or island)

## Slide 25
VIIRS-MAN Collocated 550 Comparison
VIIRS 550 retrievals over ocean are in a good agreement with MAN observations (~ 62% of VIIRS retrievals are within the MODIS expected range)
It is comparable to 64-67% MODIS retrievals are within expected range and correlation ~ 0.83-0.85 [Kleidman et al., 2012]
Liu et al, 2014
Notes: 2004-2009

## Slide 26: VIIRS AOT Retrieval Performance
 | Land |  | Ocean* | 
EDR QF | accuracy | precision | accuracy | precision
High | -0.009 | 0.130 | 0.017 | 0.068
Top2 | 0.035 | 0.154 | 0.050 | 0.081
All | 0.063 | 0.195 | 0.084 | 0.125
VIIRS Aerosol AOT retrieval versus AERONET over land (01/24/13-09/01/13) and MAN over ocean (05/02/12-12/21/13). VIIRS AOT EDR quality flag has values of high, medium, and low. Accuracy is the mean of the difference and precision is the standard deviation of the difference.

## Slide 27: Future Developments
Investigate surface reflectance relationships with NDVI-dependent relationships (surface vegetation).
Extend AOT reporting range from 2.0 to 5.0.
Update ocean aerosol models (C4) with those from latest MODIS algorithm (C5 to C6).
Improve cloud/heavy-aerosol discrimination, snow/ice detection; add spatial variability internal test.
Add Deep-Blue module (Hsu & Sayer, NASA) to extend retrievals over bright surfaces.

## Slide 28: Summary
JPSS/NPP, the US next generation of orbital satellite system, is to provide a continuation of long-term climatic observations.
The VIIRS provides information of atmospheric aerosol for the studies of global radiation budget, weather, air quality, emergency response, and climate.
The VIIRS and MODIS have similar but not the same aerosol algorithms.
VIIRS/MODIS global 550 retrieval are comparable both over land and ocean. But there is a regional difference of retrieval performance over land between VIIRS and MODIS.
The performance of VIIRS 550 retrieval with high quality EDR were compared well with in-situ measurements with accuracy of ~ 0.01 (-0.02) and R of ~ 0.8-0.9 over ocean (land).
The implementation of the deep-blue algorithm over bright surface.

## Slide 29
The articles of VIIRS aerosol CAL/VAL team on VIIRS aerosol algorithms and validations.
Jackson, J. M., H. Liu, I. Laszlo, S. Kondragunta, L. A. Remer., J. Huang., H.-C. Huang, 2013, Suomi-NPP VIIRS Aerosol Algorithms and Data Products, J. Geophys. Res., doi: 10.1002/ 2013JD020449.
Liu, H., L. A. Remer., J. Huang., H.-C. Huang., S. Kondragunta, I. Laszlo, M. Oo, J. M. Jackson, 2014, Preliminary Evaluation of Suomi-NPP VIIRS Aerosol Optical Thickness, J. Geophys. Res., accepted.

## Slide 30: Information Links
Data (EDR and IP) are available through CLASS: http://www.class.noaa.gov
Gridded data (0.25 degree) http://www.star.nesdis.noaa.gov/smcd/emb/viirs_aerosol/products_gridded.php
ATBD, Users’ guide, README file, and other documents are available through: http://www.star.nesdis.noaa.gov/smcd/emb/viirs_aerosol/documents.php

## Slide 31: Obtain VIIRS Data Online Demonstration

## Slide 32
http://www.star.nesdis.noaa.gov/smcd/emb/viirs_aerosol/index.php

## Slide 35
Sample Reader

## Slide 38
Data Access Instruction
Data Description

## Slide 41
http://www.class.ncdc.noaa.gov/saa/products

## Slide 45
Define Area
Define Time Period
Select Data

## Slide 46
Follow NOAA STAR Aerosol Web Page For Selection